## Slide 1: Optical Matched Filter
Ethan ross
OPTI 8206 Final project

## Slide 2: Introduction
What is a matched filter?
  Spatial frequency filter
  Matches image from a set of similar images
  Locates images within images
  Character recognition, wind velocities, etc.
Simple set up: 4f optical system
  Filter placed in Fourier plane
Project objective: optical character recognition
  Locate specific alphanumeric characters in input

## Slide 3: Theory: basic method
Input – front focal plane of L1
  Input = g(x,y), ℱ{input} = |G(ξ,ψ)| ejϕ(ξ,ψ)
Filter – Fourier plane
  If filter is “matched” with the input, max output at light meter.
  Filter = |G(ξ,ψ)| e-j ϕ(ξ,ψ)
If phases match, plane wave with amplitude |G(ξ,ψ)|2 will converge to light meter.
If phases do not match, will not get plane wave and will not converge to light meter.
Iizuka, Keigo. Engineering Optics. New York, NY: Springer, 2010. Print.

## Slide 4: Theory: character recognition (1)
System can also be used to locate figures within a larger image
Consider input consisting of two letters: ‘a’ and ‘b’.
  Let input = g(x,y) = a(x,y-l) + b(x,y+l)
Want to locate letter ‘a’
  Filter = A*(ξ,ψ)
In Fourier plane…
  G(ξ,ψ) A*(ξ,ψ)
Lens L2 takes FT…
  ℱ{G(ξ,ψ)}*ℱ{ A*(ξ,ψ)}
Iizuka, Keigo. Engineering Optics. New York, NY: Springer, 2010. Print.

## Slide 5: Theory: character recognition (2)
Need to simplify: ℱ {G(ξ,ψ)}*ℱ { A*(ξ,ψ)}
Duality Property of Fourier transform
  ℱ{ℱ{g(x,y)}} = g(-x,-y)
Fourier transform of conjugate w/ Duality Property
  ℱ{ A*(ξ,ψ)} = a*(x,y)
We get…
  a*(x,y)*a(-x,-y-l)+a*(x,y)*b(-x,-y+l) or
  [a(x,y)*a*(-x,-y-l)+a(x,y)*b*(-x,-y+l)]*
Iizuka, Keigo. Engineering Optics. New York, NY: Springer, 2010. Print.

## Slide 6: Theory: character recognition (3)
Convolution to correlation
  f(x,y)*g* (-x,-y)= f(x,y)★g(x,y)
Applying this, the output of the 4f system is…
First term  large peak at (0,-l)
Second term  small peak at (0,l)
Output inverted relative to input
  ‘a’ now at –l, not +l
[a(x,y)★ a(x,y-l)+a(x,y)★ b(x,y+l)]*
Iizuka, Keigo. Engineering Optics. New York, NY: Springer, 2010. Print.

## Slide 7: Test #1 in VirtualLab (1)
Demonstrated this exact system using VirtualLab

## Slide 8: Test #1 in VirtualLab (2)
FT of input
FT of target
=

## Slide 9: Test #1 in VirtualLab (3)
Final output:

## Slide 10: Test #1 in MatLAB (1)
Double check results with MatLAB
  Take cross-correlation of image and target
  Result should be identical to VirtualLab
target
input

## Slide 11: Test #1 in MatLAB (2)
Final output:

## Slide 12: Image Preparation
Saved all input images and target images as 24 bit RGB bitmap files
  Three colors: red, green, blue
  8 bits (0-255) per color
Took greyscale of each image in both VL and MatLAB before inserting into system

## Slide 13: Test #2
Now test system with a more complex input function g(x,y)
  Two paragraph input
  Locate all capital A’s

## Slide 14: Test #2 in VirtualLab
Output
Input

## Slide 15: Test #2 in MatLAB
Output
Input

## Slide 16: Test #3
Can we locate a string of characters? A word?
  Two paragraph input
  Locate all instances of the word “MATLAB”

## Slide 17: Test #3 in VirtualLab
Output
Input

## Slide 18: Test #3 in MatLAB
Output
Input

## Slide 19: Next Steps (1)
Let image input be an actual photograph
  Not totally dark background
  Complicates target matching

## Slide 20: Next Steps (2)
Even more complicated inputs
  Not alphanumeric characters
  A face?
Attempt to locate Waldo with matched filter

## Slide 21: Next Steps (3)
Complications:
  Waldo not the same in every image
  Size, expression, orientation of head, illumination, etc.
  Resulting peaks not as distinct

## Slide 24: RECAP
Demonstrated character recognition for simple and complex “binary” inputs
  Single character and a string of characters
Further exploration
  Improve matched filter with a real photographic input
    Improve target definition
  Improve matched filter with facial recognition (Waldo)
    Multiple filters

## Slide 25: Resource
Iizuka, Keigo. Engineering Optics. New York, NY: Springer, 2010. Print.

## Slide 26: Questions?